## Slide 1: Final Project Proposal
DC Lab Spring 2025
team 09 / 丁睿濂、林靖軒、劉代恩

## Slide 2: TRAIN SIMULATOR
帥哥

## Slide 3: BASIC functions
Input:
  Joystick (acceleration, brake, ...) → FPGA
  Computer (video frames & speed labels) → FPGA
Function:
  Receive control from joystick and calculate speed correspondingly
  Adjust output rate to display video according to user control
Output:
  FPGA → LCD, 7-seg display (show speed and pressure guage)
  FPGA → Monitor (show video)

## Slide 4: Hardware
joystick
Monitor
DE2-115
PC

## Slide 5: CONNECTIONS

## Slide 6: Connections
USB (joystick → FPGA): control playback speed by acceleration and brake
  Design the joystick on our own
Ethernet (PC → FPGA): send video data and speed labels
  Cat 5e cable is required, which supports transmission rate up to 1,000 Mbps
  The single Ethernet port on our PC is already occupied → USB to Ethernet adapter is required, which also supports 1,000 Mbps transmission rate
  Run Python program in PC to send and receive UDP packets to/from the FPGA
  Capable for real-time applications
VGA (FPGA → Monitor): output corresponding video
  SXGA standard (1280*1024)
  Bandwidth 100MHz

## Slide 7: Block diagram
Top
SDRAM Control
Ethernet Connection
UDP parser
PC
VGA Control
Monitor
Joystick Control
Joystick
SDRAM
7-Seg display
LCD

## Slide 8: If allowed
Train a ML model to predict speed label of the video (Ref: GitHub)
Run the ML inference on FPGA board
Record arrival time and other performances to get scored
Random weather effects, special events
Add sound for the motor sound, brake sound, and whistling sound

## Slide 9: WHY USE FPGA?
Flexibility
  Download any video and start playing after few processing
  Deal with complex protocols between FPGA and joystick
Parallel processing
  FPGAs are ideal for processing the input from joystick and PC and output to monitor
Low latency & real-time data handling
  FPGA provides faster response times, which is a fit for real-time data processing

## Slide 10: Potential issues & possible solutions
Unknown protocol between Switch and joystick
  Use logic analyzer to find the protocol of joystick → it takes a long time to decode the “private protocol” designed by Nintendo Switch
  Design our own joystick and communication protocol as a current solution
SDRAM or Ethernet does not work
  Read user manual or look up for other's experience

## Slide 11: Reference
DE2-115 User Manual
  https://www.terasic.com.tw/wiki/images/f/f2/DE2_115_manual.pdf
Ethernet
  https://medium.com/@Frank_pan/how-to-use-ethernet-components-in-fpga-altera-de2-115-26659da06362
  https://github.com/alexforencich/verilog-ethernet
SDRAM
  邏輯電路設計DE2-115實戰寶典
Vehicle Speed Estimation
  shafu0x/vehicle-speed-estimation: Vehicle Speed Estimation from Video using Deep Learning and Optical Flow in PyTorch.