## Slide 1: Final Project DEMO
DC Lab Spring 2025
team 09 / 丁睿濂、林靖軒、劉代恩

## Slide 2: Outline
Introduction
Implementation Details
  Connections
  Display
  Block Diagram
Novelty

## Slide 3: TRAIN SIMULATOR

## Slide 4: BASIC functions
Input:
  Joystick (acceleration, brake, ...) → FPGA
  Computer (video frames & speed labels) → FPGA
Function:
  Receive control from joystick and calculate speed correspondingly
  Communicate with PC to receive frames and display video accordingly
Output:
  FPGA → Monitor (show video, speed, distance, and score)

## Slide 5: CONNECTIONS
PC
Monitor
Joycon
ADC Module

## Slide 6: Connections
GPIO (joystick → FPGA): control playback speed by acceleration and brake
  Use potentiometer and ADC module (ADS1115) to communicate with FPGA
  Support I2C protocol
  Use Arduino and logic analyzer to understand the protocol:
    Initialize
    Set Config Register
      Select Config Register
      Write Config Register Settings (channel)
      Read Config Register Settings
    Read Conv Register
      Select Conv Register
      Read Conv Register

## Slide 7: Connections
Ethernet (PC → FPGA): send video frames and return speed labels
  https://github.com/alexforencich/verilog-ethernet
  Parse data packets on FPGA based on data format to handle data correctly
  Add header to packets can help FPGA distinguish different data type
  IP configuration:
    PC: 192.168.50.7
    FPGA: 192.168.50.8
    Both PC and FPGA have to be connected to the same router.
  Also supports FPGA → PC connection

## Slide 8: Connections
VGA (FPGA → Monitor): output corresponding video
Support resolution: 640*480, 30FPS
VGA_control is modified from Terasic

## Slide 9: Display
Value of basic features
  Speed: calculated from current speed and joystick’s value
  Distance to next station: send labels from PC through Ethernet
  Remaining time: counted in FPGA
Display
  Store images of 0~9 in registers

## Slide 10: Block diagram
DE2-115
SDRAM Control
Ethernet Connection
UDP parser
PC
VGA Control
Monitor
ADS
Joystick
SDRAM
7-Seg display
Speed Control
Sound Player

## Slide 11: Finite state machine

## Slide 12: novelty
Flexibility
  Download any video and start playing after few processing
  Deal with protocols between FPGA and joystick
Low latency & real-time data handling
  FPGA provides faster response times, which is a fit for real-time data processing

## Slide 13: Reference
DE2-115 User Manual
  https://www.terasic.com.tw/wiki/images/f/f2/DE2_115_manual.pdf
Ethernet
  https://medium.com/@Frank_pan/how-to-use-ethernet-components-in-fpga-altera-de2-115-26659da06362
  https://github.com/alexforencich/verilog-ethernet
SDRAM
  邏輯電路設計DE2-115實戰寶典
Vehicle Speed Estimation
  shafu0x/vehicle-speed-estimation: Vehicle Speed Estimation from Video using Deep Learning and Optical Flow in PyTorch.